## Slide 1: Principles of Radiation Therapy
Department of Surgery and Radiology
College of Veterinary Science and Animal Husbandry, DUVASU, Mathura, U.P.
Dr SANJAY PUROHIT
Prof. Sanjay Purohit – Educational & Confidential - contents – collected from different sources -not permitted for replication & commercial purposes

## Slide 2: Radiation Physics
Basis – ionizing particles interact with cellular molecules
Relies on transfer of energy created by secondary charged particles (usually electrons)
Break chemical bonds
Teletherapy vs. Brachytherapy

## Slide 3: Teletherapy
Radiation source—kept –distance from the lesion
4 types
1. Superficial X-ray therapy: Given through X-ray machine (60-100 keV)
2. Deep x-ray therapy: Given through X-ray machine 200-300 keV)
3. Super voltage therapy:
  Provided through
  X-ray machine having linear accelerator (1 -20 MeV) or Betatron (20-100 MeV) or cyclotron
  Isotopic X-ray machine with Cobalt and Cesium in a sealed form
  4. Particulate beam therapy: Electron, Proton and neutron used

## Slide 4: Brachytherapy
Radioactive source in direct contact with tumor
3 types
  1.Interstitial brachytherapy: 198Au, 60CO
  2. Pliesotherapy (Surface brachytherapy): 90Sr
  3. Systemic brachytherapy: 131I and 32P
Greater deliverable dose
Continuous low dose rate
Advantage for hypoxic or slow proliferators
Shorter treatment times

## Slide 5: Brachytherapy
Limitations
  Tumor must be accessible
  Well-demarcated
  Cannot be only modality for tumors with high risk of regional lymph node metastasis

## Slide 6: Radiobiology
Ionizing radiation ejects an electron from a target molecule
Distributed randomly within cell
Double-strand DNA breaks – lethal
Cell death: no longer able to undergo unlimited cell division
Direct vs. Indirect injury (free radicals – O2)
Inadequate cellular repair mechanisms implied

## Slide 7: Radiobiology

## Slide 8: Radiobiology
Random cell death
  Deposition of energy & injury is random event
  Same proportion of cells is damaged per dose
  100 to 10 cell reduction = 106 to 105 cell reduction
  Larger tumors require more radiation
  105 cells = nonpalpable
  Applies to normal tissue also
Therapeutic advantage – 4 R’s of radiobiology

## Slide 9: 4 R’s of radiation biology
Repair of cellular damage
Reoxygenation of the tumor
Redistribution within the cell cycle
Repopulation of cells

## Slide 10: Fractionation Schedules
Conventional
  1.8 to 2.0 Gy given 5 times/week
  Total of 6 to 8 weeks
  Effort to minimize late complications
Accelerated fractionation
  1.8 to 2.0 Gy given bid/tid
  Similar total dose (less treatment time)
  Minimize tumor repopulation (increase local control)
  Tolerable acute complications (increased)

## Slide 11: Fractionation Schedules
Hyperfractionation
  1.0 to 1.2 Gy bid/tid, 5 times/week
  Similar total treatment time (increased total dose)
  Increases total dose
  Potentially increases local control
  Same rates of late complications
  Increased acute reactions

## Slide 12
Thanks